###### Finishing a board
- Verify P/J Naming
- Add Makermod logo to bottom silk under a RAF (engunneer-helper.lbr)
- Add OSHW logo (Sparkfun-Aesthetic.lbr)
- Add board name in bottom copper “MM_BRD_NAME#” centered under RA Male plastic outline
Vector Size 45 mil 15%, Align such that text top is to edge of board, 150 mil west of double RA position. (100 mil west of single)
- Add “MakerMod” as label in Top Copper, Top Right Corner if possible
Vector Size 60 mil 14%
- Add “MakerMod” as label in Top Silk (tNames), if possible
Vector Size 80 mil 14%
- Add Version “v1.x” in Top Copper, align bottom-right (or b-left) 25 mil from corner b-r (or b-l)
Vector size 60 mil 14%
- “Run normalize-text” with 40 mil 4 mil (11%) width to make all silk text right size
- Check placement of all silk text
No Vias under silk if possible.
- Radius sharp edges 25 or 50 mil.
- Check traces for sharp corners.
- Run DRC with LaenPCB
- Final .brd file from Eagle can be submitted as-is without Gerbers to OSHpark.

TODO:
MakerMod logo in exposed copper (Top + tStop)